May 16th Field Notes.  Mount Nansen.

-Stefan Gronsdahl and Nicole Jacques

Notes to file:

-Ore on top of mill road

-clearing beyond mill on the south was the explosives storage

Weather:

-7̊C, light winds, sunny in the morning, overcast in the afternoon.

Water Samples Collected:

Ore Ramp at the south end of the pit.

Sampled at 1545h..  No water currently running.  Patches of snow remain.  There are several ponds of water.  Sample taken from below pit ramp, 10 m upgradient of the V-intersection.  Photos 1826-1827. Field preserved and filtered.(Photos: 1819-1825 show location approximately 20 m across the road from the sample location.)

Base of Waste Rock Pile (Waste Rock Pile 01)

On SW side of waste rock pile: Sampled at 1630h.  Found 1 running stream after stream after traversing many small dry channels.  The stream ran through, and on top of a snow bank, and then into an excavated trench.  Field preserved and filtered.  Photos 1828 – 1846 taken from along the base of the waste rock pile, Photos 1832-1833 show the sample location specifically.)

Lower Platform:

Sampled at 1755h.  Small stream, downstream from the road directly across from the first large mill building closest to the bunkhouse.  Stream flows through snowpack infront of mill, and braids as it crosses the road.  Hydrocarbon sheen is present near sample location in streams and on soil.  Should return with bottles suitable for sampling hydrocarbons at this location.  Field preserved and filtered. Photos 1847-1851.

Upper Platform:

Sampled at 1820h.  Small stream cut in snow from behind the first building.  Sample taken from this location because there was no running water behind the third building.  Inlet onto the flat surface is not visible, water is likely coming out of the bank.  Stream braids on the flat road surface upstream of the sample location, and then meets near sample location, just before flowing over a tin into older steel tank.  Field Preserved and filtered.  Photos: 1852: 1853.

See attached Excel spreadsheet and field forms for measurements and observations taken from wells...