COMMENTS REGARDING INTERPRETATION OF GOLD RESULTS
            -------------------------------------------------
 
  THE FOLLOWING DISCUSSION OUTLINES SOME IMPORTANT POINTS TO CONSIDER WHEN
INTERPRETING THE GOLD DATA. THIS DISCUSSION IS INCLUDED IN RECOGNITION OF
THE SPECIAL GEOCHEMICAL BEHAVIOUR AND MODE OF OCCURRENCE OF AU IN NATURE
AND THE RESULTANT DIFFICULTIES IN OBTAINING AND ANALYZING SAMPLES WHICH
REFLECT THE ACTUAL CONCENTRATION LEVEL AT A GIVEN SITE.
 
  UNDERSTANDING AU GEOCHEMICAL DATA FROM REGIONAL STREAM SEDIMENT OR
LAKE SEDIMENT SURVEYS REQUIRES AN APPRECIATION OF THE UNIQUE CHEMICAL
AND PHYSICAL CHARACTERISTICS OF AU AND ITS MOBILITY IN THE SURFICIAL
ENVIRONMENT. KEY PROPERTIES OF AU THAT DISTINGUISH ITS GEOCHEMICAL
BEHAVIOUR FROM MOST OTHER ELEMENTS INCLUDE: 
 
   1) AU OCCURS MOST COMMONLY IN THE NATIVE FORM WHICH IS CHEMICALLY
      AND PHYSICALLY RESISTANT. A HIGH PROPORTION OF THE METAL IS
      DISPERSED IN MICRON-SIZED PARTICULATE FORM. GOLD'S HIGH SPECIFIC
      GRAVITY ENSURES HETEROGENEOUS DISTRIBUTION ESPECIALLY IN STREAM
      SEDIMENT AND CLASTIC-RICH (LOW LOI) LAKE SEDIMENT ENVIRONMENTS.
      AU DISTRIBUTION APPEARS TO BE MORE HOMOGENEOUS IN ORGANIC-RICH
      FLUVIATILE AND LAKE SEDIMENT ENVIRONMENTS.
 
  2)  AU TYPICALLY OCCURS AT LOW CONCENTRATIONS IN THE PPB RANGE.
      AU CONCENTRATIONS OF A FEW PPM MAY REPRESENT ECONOMIC DEPOSITS.
      BACKGROUND LEVELS ENCOUNTERED FOR STREAM AND CENTRE-LAKE
      SEDIMENTS SELDOM EXCEED 10 PPB, AND COMMONLY ARE NEAR THE DETECTION
      LIMIT OF 1 PPB.
 
  THE MANY FOREGOING FACTORS CAN RESULT IN A PARTICLE SPARSITY EFFECT
WHEREIN VERY LOW CONCENTRATIONS OF AU ARE HETEROGENEOUSLY DISTRIBUTED IN
THE SURFICIAL ENVIRONMENT. HENCE, A MAJOR PROBLEM FACING THE GEOCHEMIST
IS OBTAINING A REPRESENTATIVE SAMPLE. IN GENERAL THE LOWER THE ACTUAL
CONCENTRATION OF AU, THE LARGER THE SAMPLE SIZE, OR THE SMALLER THE GRAIN
SIZE REQUIRED TO REDUCE UNCERTAINTY OVER WHETHER SUBSAMPLE ANALYTICAL
VALUES TRULY REPRESENT ACTUAL VALUES. CONVERSELY, AS ACTUAL AU CONCENTRATIONS
INCREASE OR GRAIN SIZE DECREASES, THE NUMBER OF AU PARTICLES TO BE SHARED IN
RANDOM SUBSAMPLES INCREASES AND THE VARIABILITY OF RESULTS DECREASES
(CLIFTON ET AL., 1969; HARRIS, 1982). THE LIMITED AMOUNT OF MATERIAL
COLLECTED DURING THE RAPID, RECONNAISSANCE-STYLE REGIONAL SURVEYS AND THE
NEED TO ANALYZE FOR A BROAD SPECTRUM OF ELEMENTS, PRECLUDES THE USE OF A
SIGNIFICANTLY LARGE SAMPLE WEIGHT FOR THE AU ANALYSES. THEREFORE, TO THE
EXTENT THAT SAMPLE REPRESENTIVITY CAN BE INCREASED, SAMPLE GRAIN SIZE IS
REDUCED BY SIEVING AND BALL MILLING OF ALL SAMPLES.
IF THE AU IS PRESENT IN A METALLIC STATE, BALL MILLING MAY NOT REDUCE
IT'S PARTICLE SIZE SIGNIFICANTLY BECAUSE OF ITS MALLEABILITY.
 
  THE FOLLOWING CONTROL METHODS ARE CURRENTLY EMPLOYED TO EVALUATE AND
MONITOR THE SAMPLING AND ANALYTICAL VARIABILITY WHICH ARE INHERENT IN THE
ANALYSIS OF AU IN GEOCHEMICAL MEDIUMS: 
 
      1) FOR EACH BLOCK OF TWENTY SAMPLES: 
 
        A) RANDOM INSERTION OF A STANDARD REFERENCE SAMPLE TO MONITOR
           AND CONTROL ANALYTICAL ACCURACY AND LONG-TERM PRECISION,
 
        B) COLLECTION OF A FIELD DUPLICATE (TWO SAMPLES SEPARATELY
           COLLECTED FROM ONE SITE) TO MONITOR SAMPLING VARIANCE,
 
        C) ANALYSIS OF A SECOND SUBSAMPLE (BLIND DUPLICATE) FROM ONE
           SAMPLE TO MONITOR AND CONTROL SHORT-TERM PRECISION;
 
      2) FOR BOTH STREAM SEDIMENTS AND LAKE SEDIMENTS, REPEAT ANALYSES
         ON A SECOND SUBSAMPLE ARE PERFORMED FOR ALL SAMPLES HAVING
         VALUES THAT ARE STATISTICALLY ABOVE APPROXIMATELY THE 90TH
         PERCENTILE OF THE TOTAL DATA SET WITHIN THE SURVEY AREA;
 
      3) FOR LAKE SEDIMENTS ONLY, REPEAT ANALYSIS ON A SECOND SUBSAMPLE
         WAS PERFORMED ON THOSE SAMPLES WITH LOI VALUES BELOW 10%,
         INDICATING A LARGE CLASTIC COMPONENT. ON-GOING STUDIES
         SUGGEST THAT THE AU DISTRIBUTION IN THESE SAMPLES IS MORE LIKELY
         TO BE HIGHLY VARIABLE THAN IN SAMPLES WITH A HIGHER LOI CONTENT.
 
 
   AU DATA PRESENTATION IS SOMEWHAT DIFFERENT THAN FOR OTHER ELEMENTS.
AU DATA INCLUDED IN THIS OPEN FILE IS IN FIVE FIELDS; INITIAL ANALYTICAL
RESULTS, REPEAT ANALYTICAL RESULTS, INITIAL SAMPLE WEIGHT, REPEAT SAMPLE
WEIGHT AND PLOT STRING. THE FIELD CALLED "PLOT STRING" WAS PLOTTED ON THE
VALUE MAPS AND IS CONSTRUCTED AS FOLLOWS. REPEAT ANALYSIS VALUES (NOT
FIELD DUPLICATES) ARE PLACED IN BRACKETS FOLLOWING THE INITIAL VALUE
DETERMINATION. ALL VALUES DETERMINED ON A SAMPLE LESS THAN 10 G ARE
DENOTED BY AN ASTERISK. ACTUAL SAMPLE WEIGHT USED CAN BE DETERMINED FROM
THE TEXT. FOLLOWING ARE SOME POSSIBLE VARIATIONS IN THE FORMAT OF THE
"PLOT STRING".
 
     *            NO DATA
 
     +27*         SINGLE ANALYSIS, <10 G SAMPLE WEIGHT
 
     +27(14)      REPEAT ANALYSIS, BOTH SAMPLES 10 G
 
     +27(14*)     REPEAT ANALYSIS, FIRST SAMPLE 10 G, REPEAT <10 G
 
     +<1          SINGLE ANALYSIS, 10 G SAMPLE, LESS THAN DETECTION LIMIT
                  OF 1 PPB
 
   IN SUMMARY, GEOCHEMICAL FOLLOW-UP INVESTIGATIONS FOR AU SHOULD BE BASED
ON A CAREFUL CONSIDERATION OF ALL GEOLOGICAL AND GEOCHEMICAL INFORMATION,
AND ESPECIALLY A CAREFUL APPRAISAL OF GOLD GEOCHEMICAL DATA AND ITS
VARIABILITY. IN SOME INSTANCES, PROSPECTIVE FOLLOW-UP AREAS MAY BE
INDIRECTLY IDENTIFIED BY PATHFINDER ELEMENT ASSOCIATIONS IN FAVOURABLE
GEOLOGY, ALTHOUGH A COMPLEMENTARY AU RESPONSE DUE TO NATURAL VARIABILITY
MAY BE LACKING. ONCE AN ANOMALOUS AREA HAS BEEN IDENTIFIED, FIELD
INVESTIGATIONS SHOULD BE DESIGNED TO INCLUDE DETAILED GEOCHEMICAL
FOLLOW-UP SURVEYS AND COLLECTION OF LARGE REPRESENTATIVE SAMPLES.
SUBSEQUENT REPEAT SUBSAMPLE ANALYSES WILL INCREASE THE RELIABILITY OF
RESULTS AND PERMIT A BETTER UNDERSTANDING OF NATURAL VARIABILITY WHICH
CAN THEN BE USED TO IMPROVE SAMPLING METHODOLOGY AND INTERPRETATION.

REFERENCES
 
CLIFTON,H.E.,HUNTER,R.E.,SWANSON,F.J.AND PHILLIPS,R.L. (1969)
        SAMPLE SIZE AND MEANINGFUL GOLD ANALYSIS. U.S. GEOLOGICAL SURVEY
        PROFESSIONAL PAPER 625-C.
 
HARRIS,J.F. (1982) SAMPLING AND ANALYTICAL REQUIREMENTS FOR EFFECTIVE USE
        OF GEOCHEMISTRY IN EXPLORATION FOR GOLD. IN LEVINSON,A.A.,EDITOR;
        PRECIOUS METALS IN THE NORTHERN CORDILLERA, PROCEEDINGS OF A
        SYMPOSIUM SPONSORED BY THE ASSOCIATION OF EXPLORATION GEOCHEMISTS
        AND THE CORDILLERAN SECTION OF THE GEOLOGICAL ASSOCIATION OF
        CANADA,PP.53-67.