GEOLOGICAL SURVEY OF CANADA OPEN FILE 1363.
REGIONAL STREAM SEDIMENT AND WATER GEOCHEMICAL RECONNAISSANCE DATA,
SOUTHWEST YUKON, NTS 115J,115K(E1/2).
 
THE RECONNAISSANCE SURVEY WAS UNDERTAKEN BY THE GEOLOGICAL SURVEY OF CANADA IN
CONJUNCTION WITH THE DEPARTMENT OF INDIAN AFFAIRS AND NORTHERN DEVELOPMENT,
AND THE GOVERNMENT OF YUKON UNDER THE CANADA-YUKON MINERAL DEVELOPMENT
AGREEMENT (1985-1989).
 
E.H.W. HORNBROOK DIRECTED THE SURVEY PROGRAM.
 
P.W.B. FRISKE COORDINATED THE OPERATIONAL ACTIVITIES OF THE CONTRACTING
AND GEOLOGICAL SURVEY OF CANADA STAFF THROUGHOUT THE SURVEY.
 
CONTRACTS LET FOR COLLECTION, SAMPLE PREPARATION AND ANALYSIS WERE THE
RESPONSIBILITY OF, AND WERE SUPERVISED AND/OR MONITORED BY THE STAFF OF THE
EXPLORATION GEOCHEMISTRY SUBDIVISION AS FOLLOWS: 
 
COLLECTION:  - MONAGHAN DELPH MILLER LTD., DON MILLS, ONTARIO
             - E.H.W. HORNBROOK, P.W.B FRISKE
 
PREPARATION: - GOLDER ASSOCIATES, OTTAWA, ONTARIO
             - J.J. LYNCH
 
ANALYSIS:    - BONDAR - CLEGG AND COMPANY LTD., OTTAWA
             - BARRINGER MAGENTA LABORATORIES (ALBERTA) LTD.,
               CALGARY,ALBERTA (WATERS)
             - CHEMEX LABS LTD.,NORTH VANCOUVER,B.C. (GOLD)
             - J.J. LYNCH, D.J. ELLWOOD
 
H.R. SCHMITT COORDINATED OPEN FILE PRODUCTION.
 
A.C. GALLETTA MANAGED THE DIGITAL GEOCHEMICAL DATA AND PROVIDED COMPUTER
PROCESSING SUPPORT.
 
D.J. ELLWOOD DEVELOPED SOFTWARE TO RASTER PLOT OPEN FILE VALUE,SYMBOL AND
REGIONAL TREND MAPS. THE PLOTTING WAS DONE BY CANADA LANDS DATA SYSTEMS
STAFF AT ENVIRONMENT CANADA, HULL QUEBEC.
 
M. MCCURDY AND S. COOK PROCESSED INCOMING AND OUTGOING MATERIALS,SUPPLIES
AND SAMPLES.
 
COMPUTING,PLOTTING, AND OPEN FILE TEXT LASER PRINTING SERVICES, WERE
PROVIDED BY THE COMPUTER SCIENCE CENTER, E.M.R.
 
J. YELLE AND F. WILLIAMS OF THE GEOLOGICAL INFORMATION DIVISION
SUPERVISED THE PREPARATION OF OPEN FILE MAPS BY CARTOGRAPHY UNIT A-2.
 
HELICOPTER AND TRUCK  SUPPORTED SAMPLE COLLECTION WAS CARRIED OUT
DURING THE SUMMER OF 1986.
STREAM SEDIMENT AND WATER SAMPLES WERE COLLECTED AT AN AVERAGE DENSITY OF ONE
SAMPLE PER 13 SQUARE KILOMETERS THROUGHOUT THE 17200 SQUARE KILOMETERS OF THE
SOUTHWESTERN YUKON SURVEY AREA.

SAMPLE SITE DUPLICATE SAMPLES WERE ROUTINELY COLLECTED IN EACH
ANALYTICAL BLOCK OF TWENTY SAMPLES.
 
IN OTTAWA, FIELD DRIED SAMPLES WERE AIR-DRIED, SIEVED THROUGH AN 80 MESH
SCREEN AND BALL MILLED. THE BALL MILLED FRACTION WAS USED FOR SUBSEQUENT
ANALYSES.
AT THIS TIME, CONTROL REFERENCE AND BLIND DUPLICATE SAMPLES WERE
INSERTED INTO EACH BLOCK OF TWENTY SEDIMENT SAMPLES. FOR THE WATER
SAMPLES,ONLY CONTROL REFERENCE SAMPLES WERE INSERTED INTO THE BLOCK.
THERE WERE NO BLIND DUPLICATE WATER SAMPLES.
 
ON RECEIPT, FIELD AND ANALYTICAL DATA WERE PROCESSED WITH THE AID OF
COMPUTERS.
THE FIELD DATA WERE RECORDED BY THE FIELD CONTRACT STAFF ON STANDARD STREAM
WATER AND SEDIMENT FIELD CARDS (REV. 74) USED BY THE GEOLOGICAL SURVEY OF CANADA
(GARRETT, 1974).
THE SAMPLE SITE POSITIONS WERE MARKED ON APPROPRIATE 1/250,000
SCALE NTS MAPS IN THE FIELD.
THESE MAPS WERE DIGITIZED AT THE GEOLOGICAL SURVEY IN OTTAWA TO OBTAIN THE
SAMPLE SITE UTM COORDINATES.
 
THE SAMPLE SITE COORDINATES WERE CHECKED AS FOLLOWS: A SAMPLE LOCATION
MAP WAS PRODUCED ON A CALCOMP 1051 DRUM PLOTTER USING THE DIGITIZED
COORDINATES; THE FIELD CONTRACTOR'S SAMPLE LOCATION MAP WAS THEN OVERLAYED
WITH THE CALCOMP MAP; THE TWO SETS OF POINTS WERE CHECKED FOR COINCIDENCE.
THE DOMINANT ROCK TYPES IN THE STREAM CATCHMENT BASINS WERE IDENTIFIED ON
APPROPRIATE GEOLOGICAL MAPS USED AS THE BEDROCK GEOLOGICAL BASE ON RGR MAPS.
 
THOROUGH INSPECTIONS OF THE FIELD AND ANALYTICAL DATA WERE MADE TO CHECK FOR ANY
MISSING INFORMATION AND/OR GROSS ERRORS.
 
QUALITY CONTROL AND MONITORING OF THE GEOCHEMICAL DATA WAS UNDERTAKEN BY A
STANDARD METHOD USED BY THE EXPLORATION GEOCHEMISTRY SUBDIVISION AT THE
GEOLOGICAL SURVEY OF CANADA.
 
FOR THE DETERMINATION OF ZN, CU, PB, NI, CO, AG, MN, FE, CD, AND AS
A 1 GRAM SAMPLE WAS REACTED WITH 3 ML CONC. HNO3 IN A TEST TUBE OVERNIGHT
AT ROOM TEMPERATURE.
AFTER DIGESTION, THE TEST TUBE WAS IMMERSED IN A HOT WATER BATH AT ROOM
TEMPERATURE AND BROUGHT UP TO 90C AND HELD AT THIS TEMPERATURE FOR 30 MINUTES
WITH PERIODIC SHAKING. 1 ML CONC. HCL WAS ADDED AND HEATING WAS CONTINUED FOR
ANOTHER 90 MINUTES.
THE SAMPLE SOLUTION WAS THEN DILUTED TO 20 ML WITH METAL FREE WATER AND MIXED.
ZN, CU, PB, NI, CO, AG, MN, FE AND CD WERE DETERMINED BY ATOMIC ABSORPTION
SPECTROSCOPY USING AN AIR-ACETYLENE FLAME.
BACKGROUND CORRECTIONS WERE MADE FOR PB, NI, CO, AG AND CD.
 
AS WAS DETERMINED BY ATOMIC ABSORPTION USING A HYDRIDE EVOLUTION METHOD
WHEREIN THE HYDRIDE(ASH3) IS EVOLVED, PASSED THROUGH A HEATED QUARTZ
TUBE IN THE LIGHT PATH OF AN ATOMIC ABSORPTION SPECTROPHOTOMETER.
THE METHOD IS DESCRIBED BY ASLIN (1976).

MOLYBDENUM AND VANADIUM WERE DETERMINED BY ATOMIC ABSORPTION SPECTROSCOPY
USING A NITROUS OXIDE ACETYLENE FLAME.
A 0.5 GRAM SAMPLE WAS REACTED WITH 1.5 ML CONCENTRATED HN03 AT 90C FOR 30
MINUTES.
AT THIS POINT 0.5 ML CONCENTRATED HCL WAS ADDED AND THE DIGESTION WAS CONTINUED
AT 90C FOR AN ADDITIONAL 90 MINUTES.
AFTER COOLING, 8 ML OF 1250 PPM AL SOLUTION WERE ADDED AND THE SAMPLE SOLUTION
WAS DILUTED TO 10 ML BEFORE ASPIRATION.
 
MERCURY WAS DETERMINED BY THE HATCH AND OTT PROCEDURE WITH SOME MODIFICATIONS.
THE METHOD IS DESCRIBED BY JONASSON ET AL. (1973).
A 0.5 GRAM SAMPLE WAS REACTED WITH 20 ML CONCENTRATED HNO3 AND 1 ML CONCENTRATED
HCL IN A TEST-TUBE FOR 10 MINUTES AT ROOM TEMPERATURE PRIOR TO 2 HOURS OF
DIGESTION WITH MIXING AT 90C IN A HOT WATER BATH.
AFTER DIGESTION, THE SAMPLE SOLUTIONS WERE COOLED AND DILUTED TO 100 ML WITH
METAL FREE WATER.
THE HG PRESENT WAS REDUCED TO THE ELEMENTAL STATE BY THE ADDITION OF 10 ML 10%
W/V SNSO4 IN M H2SO4.
THE HG VAPOUR WAS THEN FLUSHED BY A STREAM OF AIR INTO AN ABSORPTION CELL
MOUNTED IN THE LIGHT PATH OF AN ATOMIC ABSORPTION SPECTROPHOTOMETER.
ABSORPTION MEASUREMENTS WERE MADE AT 253.7 NM.
 
LOSS ON IGNITION WAS DETERMINED USING A 500 MG SAMPLE.
THE SAMPLE, WEIGHED INTO 30 ML BEAKER, WAS PLACED IN A COLD MUFFLE FURNACE
AND BROUGHT UP TO 500C OVER A PERIOD OF 2-3 HOURS.
THE SAMPLE WAS LEFT AT THIS TEMPERATURE FOR 4 HOURS, THEN ALLOWED TO COOL
TO ROOM TEMPERATURE FOR WEIGHING.
 
URANIUM WAS DETERMINED USING A NEUTRON ACTIVATION METHOD WITH
DELAYED NEUTRON COUNTING.
A DETAILED DESCRIPTION OF THE METHOD IS PROVIDED BY BOULANGER ET AL(1975).
IN BRIEF, A 1 GRAM SAMPLE WAS WEIGHED INTO A 7 DRAM POLYETHYLENE VIAL,
CAPPED AND SEALED.
THE IRRADIATION WAS PROVIDED BY THE SLOWPOKE REACTOR WITH AN OPERATING
FLUX OF 5** 10 NEUTRONS/SQ.CM./SEC.
THE SAMPLES WERE PNEUMATICALLY TRANSFERRED FROM AN AUTOMATIC LOADER TO
THE REACTOR, WHERE EACH SAMPLE WAS IRRADIATED FOR 20 SECONDS.
AFTER IRRADIATION, THE SAMPLE WAS AGAIN TRANSFERRED PNEUMATICALLY TO THE
COUNTING FACILITY WHERE AFTER A 10 SECOND DELAY THE SAMPLE WAS COUNTED
FOR 20 SECONDS WITH SIX HELIUM DETECTOR TUBES EMBEDDED IN PARAFFIN.
FOLLOWING COUNTING,THE SAMPLES WERE AUTOMATICALLY EJECTED INTO A
SHIELDED STORAGE CONTAINER.
CALIBRATION WAS CARRIED OUT ONCE A DAY AS A MINUMUM, USING NATURAL
MATERIALS OF KNOWN URANIUM CONCENTRATION.

FLUORINE WAS DETERMINED IN STREAM SEDIMENTS AS DESCRIBED BY FICKLIN (1970).
A 250 MG SAMPLE WAS SINTERED WITH 1 GRAM OF A FLUX CONSISTING OF TWO PARTS BY
WEIGHT SODIUM CARBONATE AND 1 PART BY WEIGHT POTASSIUM NITRATE.
THE RESIDUE WAS THEN LEACHED WITH WATER, THE SODIUM CARBONATE WAS NEUTRALIZED
WITH 10 ML 10% (W/V) CITRIC ACID AND THE RESULTING SOLUTION WAS DILUTED
TO 100 ML WITH WATER.
THE PH OF THE RESULTING SOLUTION SHOULD BE FROM 5.5 TO 6.5.
THE FLUORIDE CONTENT OF THE TEST SOLUTION WAS THEN MEASURED USING A FLUORIDE ION
ELECTRODE.
STANDARD SOLUTIONS CONTAIN SODIUM CARBONATE AND CITRIC ACID IN THE SAME
QUANTITIES AS THE SAMPLE SOLUTION.
A DETECTION LIMIT OF 40 PPM WAS ACHIEVED.
 
GOLD WAS DETERMINED USUALLY ON A 10 GRAM STREAM SEDIMENT SAMPLE;
DEPENDING ON THE AMOUNT OF SAMPLE AVAILABLE,LESSER
WEIGHTS WERE SOMETIMES USED. THIS RESULTED IN A VARIABLE DETECTION
LIMIT:1 PPB FOR A 10 GRAM SAMPLE,2 FOR A 5 GRAM SAMPLE... THE SAMPLE WAS
FUSED TO PRODUCE A LEAD BUTTON, COLLECTING ANY GOLD IN THE SAMPLE, WHICH
WAS CUPELLED IN A MUFFLE FURNACE TO PRODUCE A SILVER(DORE) BEAD. THE
SILVER BEADS WERE IRRADIATED IN A NEUTRON FLUX FOR 1 HOUR,COOLED FOR 4
HOURS,AND COUNTED BY GAMMA RAY SPECTROMETRY.CALIBRATION WAS CARRIED OUT
USING STANDARD AND BLANK BEADS.
 
TUNGSTEN WAS DETERMINED AS FOLLOWS: A 0.2 GRAM SAMPLE OF STREAM SEDIMENT WAS
FUSED WITH 1 GRAM K2S2O7 IN A RIMLESS TEST TUBE AT 575C FOR 15 MINUTES IN A
FURNACE. THE COOLED MELT WAS THEN LEACHED WITH 10 ML CONCENTRATED HCL IN A
WATER BATH HEATED TO 85C. AFTER THE SOLUBLE MATERIAL HAD COMPLETELY DISSOLVED,
THE INSOLUBLE MATERIAL WAS ALLOWED TO SETTLE AND AN ALIQUOT OF 5 ML WAS
TRANSFERRED TO ANOTHER TEST TUBE. 5 ML OF 20% SNCL2 SOLUTION WERE THEN ADDED TO
THE SAMPLE ALIQUOT,MIXED AND HEATED FOR 10 MINUTES AT 85C IN A HOT WATER BATH.
A 1 ML ALIQUOT OF DITHIOL SOLUTION ( 1% DITHIOL IN ISO-AMYL ACETATE) WAS ADDED
TO THE TEST SOLUTION AND THE TEST SOLUTION WAS THEN HEATED FOR 4-6 HOURS AT
80-85C IN A HOT WATER BATH. THE TEST SOLUTION WAS THEN REMOVED FROM THE HOT
WATER BATH,COOLED AND 2.5 ML OF KEROSENE ADDED TO DISSOLVE THE GLOBULE.
THE COLOUR INTENSITY OF THE KEROSENE SOLUTION WAS MEASURED AT 630 NM
USING A SPECTROPHOTOMETER.
THE METHOD IS DESCRIBED BY QUIN AND BROOKS (1972).
 
TIN IN STREAM SEDIMENTS WAS DETERMINED AS FOLLOWS:A 200 MG SAMPLE WAS
HEATED WITH  NH4I;THE SUBLINED SNI4 WAS DISSOLVED IN ACID AND THE TIN
DETERMINED BY ATOMIC ABSORPTION SPECTROMETRY.
 
ANTIMONY WAS DETERMINED IN STREAM SEDIMENTS AS DESCRIBED BY (ASLIN,1976).
A 500 MG SAMPLE WAS PLACED IN A TEST TUBE; 3 ML CONCENTRATED HNO3 AND
9 ML CONCENTRATED HCL ARE ADDED AND THE MIXTURE WAS ALLOWED TO STAND
OVERNIGHT AT ROOM TEMPERATURE.THE MIXTURE WAS HEATED SLOWLY TO 90C AND
MAINTAINED AT THIS TEMPERATURE FOR AT LEAST 90 MINUTES.
THE SOLUTION WAS COOLED AND DILUTED TO 10 ML. A 400 MICRO L ALIQUOT OF
THIS TEST SOLUTION WAS REMOVED AND DILUTED TO 10 ML WITH 1.8M HCL.THE
ANTIMONY IN AN ALIQUOT OF THIS DILUTE SOLUTION WAS THEN DETERMINED BY HYDRIDE
EVOLUTION-ATOMIC ABSORPTION SPECTROMETRY .

BARIUM WAS DETERMINED AS FOLLOWS: A 0.25 GRAM SAMPLE WAS HEATED WITH
5 ML CONC. HF, 5 ML CONC. HCLO4 AND 2 ML CONC. HNO3 TO FUMES OF HCLO4;
3 ML OF CONC. HCLO4 WERE ADDED AND HEATED TO LIGHT FUMES; 5 ML OF WATER
WERE ADDED AND THE SOLUTION WAS TRANSFERRED TO A CALIBRATED TEST TUBE AND
DILUTED TO 25 ML WITH WATER. BARIUM WAS DETERMINED BY ATOMIC ABSORPTION
SPECTROSCOPY USING A NITROUS OXIDE ACETYLENE FLAME.
 
FLUORIDE IN STREAM WATER SAMPLES WAS DETERMINED USING A FLUORIDE ELECTRODE.
PRIOR TO MEASUREMENT AN ALIQUOT OF THE SAMPLE WAS MIXED WITH AN EQUAL VOLUME
OF TISAB II SOLUTION (TOTAL IONIC STRENGTH ADJUSTMENT BUFFER).
THE TISAB II BUFFER SOLUTION WAS PREPARED AS FOLLOWS: 58 GM NACL
AND 5 GM  CDTA (CYCLOHEXYLENE DINITRILO ACETIC ACID) WERE DISSOLVED IN A
MIXTURE OF 50 ML METAL FREE WATER AND 57 ML GLACIAL ACETIC ACID. THE
SOLUTION WAS COOLED TO ROOM TEMPERATURE AND THE PH ADJUSTED TO BETWEEN
5.0 AND 5.5 BY NTHE SLOW ADDITION OF 5M NAOH SOLUTION. THE SOLUTION WAS
COOLED AND DILUTED TO 1 LITER IN A VOLUMETRIC FLASK.
 
HYDROGEN ION ACTIVITY (PH) WAS MEASURED WITH A COMBINATION GLASS-CALOMEL
ELECTRODE AND A PH METER.
 
URANIUM IN WATERS WAS DETERMINED BY A LASER-INDUCED FLUOROMETRIC METHOD
USING A SCINTREX UA-3 URANIUM ANALYSER.
A COMPLEXING AGENT, KNOWN COMMERCIALLY AS FLURAN AND COMPOSED OF SODIUM
PYROPHOSPHATE AND SODIUM MONOPHOSPHATE, (HALL, G.E.M., 1979) WAS ADDED TO
PRODUCE THE URANYL PYROPHOSPHATE SPECIES WHICH FLUORESCES WHEN EXPOSED
TO THE LASER.
SINCE ORGANIC MATTER IN THE SAMPLE CAN CAUSE UNPREDICTABLE BEHAVIOUR, A STANDARD
ADDITION METHOD WAS USED.
FURTHER, THERE HAVE BEEN INSTANCES AT THE G.S.C. WHERE THE REACTION OF URANIUM
WITH FLURAN IS EITHER DELAYED OR SLUGGISH; FOR THIS REASON AN ARBITRARY 24 HOUR
TIME DELAY BETWEEN THE ADDITION OF THE FLURAN AND THE ACTUAL READING WAS
INCORPORATED INTO THIS METHOD.
IN PRACTICE,500 UL OF FLURAN SOLUTION WERE ADDED TO A 5 ML SAMPLE AND ALLOWED TO
STAND FOR 24 HOURS. AT THE END OF THIS PERIOD FLUORESCENCE READINGS WERE MADE
WITH THE ADDITION OF 0.0, 0.2 AND 0.4 PPB U.
FOR HIGH SAMPLES THE ADDITIONS WERE 0.0, 2.0 AND 4.0 (20 UL ALIQUOTS OF EITHER
55 OR 550 PPB U WERE USED).
ALL READINGS WERE TAKEN AGAINST A SAMPLE BLANK.

REFERENCES
 
ASLIN, G.E.M. (1976) THE DETERMINATION OF ARSENIC AND ANTIMONY IN GEOLOGICAL
        MATERIALS BY FLAMELESS ATOMIC ABSORPTION SPECTROPHOTOMETER
        JOURNAL OF GEOCHEMICAL EXPLORATION, VOL. 6,PP. 321-330.
 
BOULANGER, A., EVANS, D.J.R. AND RABY, B.F. (1975) URANIUM ANALYSIS BY NEUTRON
        ACTIVATION DELAYED NEUTRON COUNTING: PROC. OF THE 7TH ANNUAL SYMP. OF
        CANADIAN MINERAL ANALYSTS.  THUNDER BAY, ONTARIO, SEPT. 22-23, 1975.
 
CLIFTON,H.E.,HUNTER,R.E.,SWANSON,F.J.AND PHILLIPS,R.L. (1969)
        SAMPLE SIZE AND MEANINGFUL GOLD ANALYSIS. U.S. GEOLOGICAL SURVEY
        PROFESSIONAL PAPER 625-C.
 
FICKLIN, W.H. (1970)  A RAPID METHOD FOR THE DETERMINATION OF FLUORIDE IN ROCKS
        AND SOILS, USING AN ION SELECTIVE ELECTRODE.  U.S. GEOL. SURV.
        PAPER 700C PP. C186-188.
 
GARRETT, R.G. (1974) FIELD DATA AQUISITION METHODS FOR APPLIED GEOCHEMICAL
        SURVEYS AT THE GEOLOGICAL SURVEY OF CANADA: GEOL SURV. CAN. PAPER 74-52.
 
HALL, G.E.M. (1979) A STUDY OF THE STABILITY OF URANIUM IN WATERS COLLECTED
        FROM VARIOUS GEOLOGICAL ENVIRONMENTS IN CANADA; IN CURRENT
        RESEARCH, PART A, GEOL. SURV. CAN. PAPER 79-1A, P. 361-365.
 
HARRIS,J.F. (1982) SAMPLING AND ANALYTICAL REQUIREMENTS FOR EFFECTIVE USE
        OF GEOCHEMISTRY IN EXPLORATION FOR GOLD. IN LEVINSON,A.A.,EDITOR;
        PRECIOUS METALS IN THE NORTHERN CORDILLERA, PROCEEDINGS OF A
        SYMPOSIUM SPONSORED BY THE ASSOCIATION OF EXPLORATION GEOCHEMISTS
        AND THE CORDILLERAN SECTION OF THE GEOLOGICAL ASSOCIATION OF
        CANADA,PP.53-67.
 
JONASSON, I.R., LYNCH,J.J. AND TRIP, L.J. (1973) FIELD AND LABORATORY
        METHODS USED BY THE GEOLOGICAL SURVEY OF CANADA IN
        GEOCHEMICAL SURVEYS: NO. 12, MERCURY IN ORES, ROCKS,SOILS,
        SEDIMENTS AND WATER:  GEOL. SURV. CAN. PAPER 73-21.
 
QUIN,B.F. AND BROOKS,R.R.(1972) THE RAPID DETERMINATION OF TUNGSTEN
        IN SOILS, STREAM SEDIMENTS, ROCKS AND VEGETATION. ANAL.CHIM.
        ACTA. 58 PP 301-309.