MINISTRY OF ENERGY, MINES AND PETROLEUM RESOURCES  Mineral Resources Division  Geological Survey Branch  Environmental Geology Section   File :   104M.DOC   Date :   August 4, 1993REGIONAL GEOCHEMICAL SURVEY - DIGITAL DATABC RGS 37  -  NTS 104M  Skagway ...INTRODUCTIONOpen File BC RGS 37 was published on August 4, 1993 as part of the British Columbia Regional Geochemical Survey (RGS) Program.  This Open File DISKETTE includes analytical and field data compiled from a reconnaissance scale stream-sediment and water survey conducted in NTS map sheet 104M - Skagway during the 1992 field season.  Adjacent NTS map sheets 1140 - Yakutat and 114P - Tatshenshini were also surveyed as part of the 1992 RGS field program.  The 1992 surveys and production of Open File BC RGS 37 were managed by the British Columbia Ministry of Energy, Mines and Petroleum Resources (MEMPR) and are a contribution to the Corporate Resource Inventory Initiative (CRII).  Analytical data and field observations compiled by the RGS Program are used in the development of a high quality geochemical database suitable for resource assessment, mineral exploration, geological mapping and environmental studies.  Sample collection, preparation and analysis are closely monitored by the MEMPR to ensure consistency and conformance to national standards.ACKNOWLEDGMENTSThe RGS Program is managed by Geological Survey Branch staff of the MEMPR.  P.F. Matysek and W. Jackaman  coordinated the operational activities of contract and MEMPR staff.  W. Jackaman  monitored the field program and produced this Open File.  COLLECTION :	McElhanney Engineering Services Ltd., Surrey, B.C.PREPARATION :	Rossbacher Laboratories Ltd., Burnaby, B.C.ANALYSIS :	Barringer Laboratories Ltd., Calgary, Alta.		(sediments)		Activation Laboratories Ltd., Ancaster, Ont. 		(INAA - sediments)		Chemex Laboratories Ltd., North Vancouver, B.C. 		(waters)SURVEY DETAILSPhysiography and GeologySituated in the northwest corner of British Columbia, NTS map sheet 104M - Skagway includes the Coast Mountain and Tagish Highland physiographic subdivisions (Holland, 1976).  Trending southeast to northwest, the Coast Mountains extend along the western portion of the map sheet and are characterized by rugged mountain peaks separated by numerous glaciers and snowfields.  Bordering the Coast Mountains to the northeast is a transition zone (Tagish Highlands) between the Coast Mountains and the Yukon Plateaus.  The Tagish Highlands contains relatively smooth and gently sloping mountains separated by wide, U-shaped valleys.  The survey area presently contains 87 recorded mineral occurrences and is best known for the Gridiron, Ben-My-Chree and Engineer gold-silver past producers.  Underlain  by the Intermontane and Coast Crystalline tectonic belts, potential exploration targets include precious metal vein deposits, gold-quartz veins, gold-stibnite veins, auriferous quartz-carbonate zones and gold rich skarns.  The bedrock geology base map used in Open File BC RGS 37 is modified from an unpublished compilation by Mihalynuk and Smith, 1993 (Table 1).Table 1. Bedrock Geology Legend - NTS 104M QUATERNARY DEPOSITS  Qal       Extensive areas of unconsolidated            glacial till and poorly sorted            alluvium.    INTRUSIVE ROCKS  eTg,eTgd  Coast plutonic complex, dominantly             granodiorite and other undifferentiated            granitoids.  KTg       Late Cretaceous to Eocene granitoid rocks             of the Coast Mountains, undifferentiated.  lKg,lKgd  Late Cretaceous undifferentiated granitoid             rocks; granodiorite. Mainly associated             with the Coast plutonic complex.  Kg,Kqm    Undifferentiated Cretaceous granitoid             rocks. In part equivalent to lKg.  eKg, eKt  Early Cretaceous undifferentiated granitoid             rocks; tonalite.  mlJg      Middle or late Jurassic granotoids.  eJgd,eJh  Hale Mountain granodiorite and related(?)             hornblendite (184-187 Ma).    lTgd,lTg  Granodiorite, minor leucogranite, quartz   lThg      diorite, and gabbro of late Triassic age.             May be altered or slightly deformed.             Includes the Bennett pluton.  PTgd      Permo-Triassic(?) intrusive rocks of unknown             affinity.       LATE MESOZOIC/TERTIARY EXTRUSIVE ASSEMBLAGES  Es        Skukum volcanic suite; mainly intra-caldera            facies dominated by intermediate to felsic             tuffs and flows of Eocene age.  eEs       Sloko Group, undivided, aerially extensive             rhyolite to andesite breccia and tuff of             Early Eocene age.  Pt        Tagish volcanic suite; dominantly intra-            caldera megabreccia and intermediate to             felsic tuffs and flows of Paleocene age.  Km        Montana Mountain suite. Mainly intermediate             to felsic tuffs and flows.  lKtv      Windy-Table volcanic suite. Quartz-phyric             ash flows and intermediate breccia and tuff.  lmJv      Tutshi volcanic suite. Basalt to dacite             flows and tuff of interpreted lower to             middle Jurassic age.  lJL       Laberge Group undifferentiated.  Includes             siltstone, arenaceous greywacke, argillite,             and conglomerate of Early Jurassic age.    lJLg    Laberge Group; mainly medium to coarse,             quartz-bearing wacke.    lJLa    Laberge Group; mainly argillite with             subordinate siltstone and wacke.         OLDER VOLCANIC ASSEMBLAGES, SEDIMENTARY,                  AND METAMORPHIC ROCKS    STIKINE(?) TERRANE   uTs       Stuhini Group, undifferentiated.  Includes             feldspar-phyric and pyroxene-phyric flows,             tuff, tuffite, and breccia; conglomerate,             limestone, argillite.    uTss    Stuhini Group; dominated by volcanic derived             sediments of coarse conglomerate to silty             argillite composition.    uTsv    Stuhini Group; dominated by bladed             plagioclase and pyroxene-phyric flows rocks             (lower) or intermediate tuffs (higher in             section).  PPmb      Boundary Ranges metamorphic suite,             undifferentiated:  Metamorphosed siltstone,             greywacke, tuff, greenstone, and limestone             metamorphosed to transitional greenschist-            amphibolite facies, regionally retrograded.              Current data permits a Permian to Devonian             age.    CACHE CREEK TERRANE  MTc       Undifferentiated Cache Creek Complex.            Sheared melange consisting of pods of             ultramafic rocks, greenstone, marble, chert,             and clastics in a sheared matrix of             greywacke and argillite. Mississippian to             Late Triassic age.    MTCs    Mainly pelagic and hemipelagic sediments     MTCl    Mainly limestone     MTCb    Pillow basalt, gabbro and minor ultramafic             tectonite.  TP        Undivided Peninsula Mountain volcano-            sedimentary suite. Includes basaltic to             rhyolitic tuff, breccia and tuff of Middle             to Late Triassic age.    NISLING TERRANE?  PPgn      Florence Range Metamorphic Suite.  Includes             semipelitic, pelitic, carbonate, amphibolite             and calcsilicate schist and gneiss.             Paleozoic and Late Proterozoic protoliths             are most likely.  PMgn      Gneiss and schist; age and affinity             uncertain, but possibly Mezozoic or older.Sample Collection Helicopter and truck-supported sample collection was carried out during July and August of 1992.  A total of 785 stream sediment and 773 stream water samples were systematically collected from 741 sites.  Average sample site density was 1 site per 10 square kilometres over the 7500 square kilometre survey area.  One field duplicate sample was routinely collected in each analytical block of twenty samples.  The survey also included the collection of 43 sediment and water samples in Atlin Provincial Park and Recreation Area.The majority of primary and secondary drainage basins having catchment areas of less than 10 square kilometres were sampled.  At each site sediment samples weighing 1 to 2 kilograms were collected within the active (subject to annual flooding) stream channel and placed in kraft-bags.  Samples were primarily composed of fine-grained material mixed with varying amounts of coarse sand and gravel, glacial sediments and organic material.  Contaminated or poor-quality sample sites were avoided by choosing an alternate stream or by sampling a minimum of 60 metres upstream from the identified source of contamination.  In order to minimize the glacial flour component of samples collected from glacial streams, the coarser grained material below the surface layer was sampled.  Unfiltered water samples free of suspended material were collected in 250-millilitre bottles.  Field observations regarding sample media, sample site and local terrain were also recorded. To assist follow-up, aluminum tags inscribed with a RGS sample site identification number (ie. 921002) were fixed to permanent objects, when available, at each site.Recorded field observations (Appendix A) indicate that 14 per cent of the sample sites are located in the Coast Mountains (youthful mountains).  Creeks found in this area tend to be fast flowing and are often charged with sediments from melting ice.  A total of 311 sites list glacial melt water as the stream water source.  Over 80 per cent of the sample sites are located within areas characterized by mature mountains (Tagish Highlands).  This region contains creeks which tend to be slower flowing and produce sediment material with a slightly higher organic composition.  Sediment samples collected in the Tagish Highland average 6.1 per cent loss on ignition and only 3.3 per cent loss on ignition for samples collected in areas listed as youthful mountains.  The overall stream width and depth at each sample site average 5.0 metres and 85 centimetres respectively.  Sample Preparation At a field camp established in Atlin, sediment samples were air-dried at a temperature range of 30¡C to less than 50¡C and material finer than 1 mm was recovered by sieving each sample through a -18 mesh ASTM screen.  Samples were shipped to Rossbacher Laboratories Ltd. (Burnaby, B.C.) for final processing.  The -80 mesh (<177 microns) fraction was obtained for analyses by dry sieving each sample.  Quality control reference standards and analytical duplicate samples were inserted into each analytical block of twenty sediment samples.  A quantity of -80 mesh material and a representative sample of the +80 to -18 mesh fraction was archived for future studies.  Control reference water standards were inserted into each analytical block of 20 water samples. Sample Analysis - Routine Analytical SuiteBarringer Laboratories Ltd. (Calgary, Alta.) analyzed the sediment samples for antimony, arsenic, bismuth, cadmium, cobalt, copper, fluorine, iron, lead, manganese, mercury, molybdenum, nickel, silver, vanadium, zinc and loss on ignition.  Water samples were analyzed for fluoride, uranium, sulphate and pH by Chemex Laboratories Ltd. (North Vancouver, B.C.).  Laboratory reported detection limits for each element are listed in Table 2.  Table 2. RGS suite of elements: NTS 104M          Detection                     Detection Element   Limit     Method    Element   Limit     MethodAntimony   0.2 ppm  AAS       Gold       2   ppb  INAAArsenic    0.2 ppm  AAS-H     Antimony   0.1 ppm  INAABismuth    0.2 ppm  AAS-H     Arsenic    0.5 ppm  INAACadmium    0.2 ppm  AAS       Barium     50  ppm  INAACobalt     2   ppm  AAS       Bromine    0.5 ppm  INAACopper     2   ppm  AAS       Cerium     3   ppm  INAAFluorine   40  ppm  ION       Cesium     1   ppm  INAAIron       0.02 %   AAS       Chromium   5   ppm  INAALead       2   ppm  AAS       Cobalt     1   ppm  INAAManganese  5   ppm  AAS       Hafnium    1   ppm  INAAMercury    10  ppb  AAS-F     Iron       0.02 %   INAAMolybdenum 1   ppm  AAS       Lanthanum  1   ppm  INAANickel     2   ppm  AAS       Lutetium  0.05 ppm  INAASilver     0.2 ppm  AAS       Molybdenum 1   ppm  INAAVanadium   5   ppm  AAS       Nickel     20  ppm  INAAZinc       2   ppm  AAS       Rubidium   15  ppm  INAALOI        1.0  %   GRAV      Samarium   0.1 ppm  INAA                              Scandium   0.1 ppm  INAAFluoride   20  ppb  ION       Sodium     0.01 %   INAAUranium    0.05ppb  LIF       Tantalum   0.5 ppm  INAASulphate   1   ppm  TURB      Terbium    0.5 ppm  INAApH         0.1      GCE       Thorium    0.5 ppm  INAA                              Tungsten   1   ppm  INAA                              Uranium    0.5 ppm  INAA                              Ytterbium  0.2 ppm  INAAAntimony was determined as described by Aslin (1976).  A 0.5 gram sample was placed in a test tube with 3 ml concentrated HNO3 and 9 ml HCl.  The mixture was allowed to stand overnight at room temperature prior to being heated to 90¡C and maintained at this temperature for 90 minutes.  The mixture was cooled and a 1 ml aliquot was diluted to 10 ml with 1.8M HCl.  This dilute solution was determined by hydride evolution-atomic absorption spectroscopy (AAS).Arsenic and bismuth were determined on a 1 gram sample reacted with 3 ml of concentrated HNO3 for 30 minutes at 90¡C.  Concentrated HCl (1 ml) was added and the digestion was continued at 90¡C for an additional 90 minutes.  A 1 ml aliquot was diluted to 10 ml with 1.5M HCl in a clean test tube.  The diluted sample solution was added to a sodium borohydride solution and aspirated through a heated quartz tube in the light path of an atomic absorption spectrometer (AAS-H).For the determination of cadmium, cobalt, copper, iron, lead, manganese, nickel, silver, and zinc, a 1 gram sample was reacted with 3 ml of concentrated HNO3 for 30 minutes at 90¡C.  Concentrated HCl (1 ml) was added and the digestion was continued at 90¡C for an additional 90 minutes.  The sample solution was then diluted to 20 ml with metal free water and mixed.  Concentrations were determined by AAS using an air-acetylene flame.  Background corrections were made for Pb, Ni, Co and Ag.Fluorine was determined as described in Ficklin (1970).  A 0.25 gram sample was sintered with a 1 gram flux consisting of 2 parts by weight Na2CO3 and 1 part by weight KNO3.  The residue was then leached with water and the Na2CO3  was neutralized with 10 ml 10% (w/v) citric acid.  The resulting solution was diluted to 100 ml with water to a pH of 5.5 to 6.5 and measured using a fluoride ion electrode (ION).Mercury was determined using a 0.5 gram sample reacted with 20 ml concentrated HNO3 and 1 ml concentrated HCl in a test tube for 10 minutes at room temperature and for 2 hours in a 90¡C water bath.  After digestion the sample was cooled and diluted to 100 ml with metal free water.  The Hg present was reduced to the elemental state by the addition of 10 ml of 10% w/v SnSO4 in H2SO4.  The Hg vapor was flushed by a stream of air into an absorption cell mounted in the light path of an atomic absorption spectrometer (AAS-F).  Measurements were made at 253.7 nm.  This method is described by Jonasson, et al. (1973).Molybdenum and vanadium were determined by AAS using nitrous oxide acetylene flame.  A 0.5 gram sample was reacted with 1.5 ml concentrated HNO3 at 90¡C for 30 minutes. At this point 0.5 ml of concentrated HCl was added and the digestion continued for an additional 90 minutes.  After cooling, 8 ml of 1250 ppm Al solution was added and the sample solution diluted to 10 ml before aspiration by AAS.Loss on ignition was determined using a 0.5 gram sample. The sample was weighed into a 30 ml beaker, placed in a cold muffle furnace and heated to 500¡C over a period of 2 to 3 hours.  The sample was left at this temperature for 4 hours, then cooled to room temperature before weighing (GRAV).Fluoride in waters was determined using a specific ion electrode.  An aliquot of sample was mixed with an equal volume of total ionic strength adjustment buffer (TISAB II solution).  The fluoride was measured using a Corning 101 Electrometer with an Orion Fluoride Electrode (ION).Uranium in waters was determined by a fluorometric method. The U was initially preconcentrated by evaporation. The residue was fused with a mixture of Na2CO3, K2CO3 and NaF in a platinum dish. After cooling the fluorescence of the fused pellet was measured using a Turner Fluorometer (LIF).Sulphate in waters was determined on 50 ml sample mixed with 0.3 ml of Sulfaver IV reagent.  The solution is poured into a spectrometer absorption cell and the turbidity is measured at 420 nm (TURB).pH in waters was measured using an aliquot of sample in a clean dry beaker by a Fisher Accumet pH Meter (GCE).Sample Analysis - INAAThe determination of gold, antimony, arsenic, barium, bromine, cerium, cesium, chromium, cobalt, hafnium, iron, lanthanum, lutetium, molybdenum, nickel, rubidium, samarium, scandium, sodium, tantalum, terbium, thorium, tungsten, uranium and ytterbium by INAA was conducted by Activation Laboratories Ltd. (Ancaster, Ont.).  This analytical technique involves irradiating the sediment samples, which on average weigh 15 grams, for 20 minutes in a neutron flux of 1011 neutrons/cm2/second.  After a decay period of approximately 1 week, gamma-ray emissions for the elements were measured using a gamma-ray spectrometer with a high resolution, coaxial germanium detector. Counting time was approximately 15 minutes per sample and the results were compiled on a computer and later converted to concentrations.  Table 2 lists the associated laboratory reported detection limits for this analytical technique.Repeat analysis by INAA have also been performed on a separate split for samples reporting gold values exceeding 23 ppb and are listed as Au2 in Appendix A..  This level represents the 95th percentile for gold based on the total 1992 analytical data set (NTS map sheets 104M, 114O and 114P).  INTERPRETATION OF GOLD DATAUnderstanding gold geochemical data from regional stream sediment surveys requires an understanding of the chemical and physical characteristics of gold in the surficial environment.Gold is a soft, malleable element of high density (19.3 g/cm3).  Gold is chemically inert and commonly occurs in native form (pure Au) or as electrum (alloyed with silver).  Sub-micron sized gold is often bound to clays, adsorbed onto Fe-Mn oxides or contained within organic colloids.  At normal surface temperatures, gold will dissolve under rare conditions of high oxidation potential and high acidity where ions such as chloride (Cl-), thiosulphate (S2O3-2) or cyanide (CN-) are present. Normal background concentrations for gold in bedrock vary, but are generally less than 5 ppb.  Background levels encountered for stream sediments seldom exceed 10 ppb and commonly are near the detection limit of 2 ppb.  Gold generally occurs as rare, discrete particles. In many instances a geochemical subsample may or may not contain a gold grain.  This is known as the 'nugget effect'. Generally, larger geochemical sample sizes are required to minimize the nugget effect and more accurately represent gold concentrations. (Clifton et al., 1969; Harris, 1982). Neutron activation analyses for the 1992 RGS analytical program utilized samples weighing on average 15 grams.  Follow-up investigations of gold anomalies should be based on careful consideration of related geological and geochemical information and an understanding of the variability of gold geochemical data.  Once an anomalous area has been identified, field investigations should be designed to include detailed geochemical follow-up surveys and collection of large, representative samples.  Analysis of field and analytical duplicate samples enables assessment of the reliability of gold results and permits better data interpretation.REFERENCESAslin, G.E.M. (1976): The Determination of Arsenic and Antimony in 	Geological Materials by Flameless Atomic Absorption 	Spectrophotometry; Journal of Geochemical Exploration, Volume 	6, pp. 321-330.Clifton, H.E., Hunter, R.E., Swanson, F.J. and Phillips, R.L. 	(1969): Sample Size and Meaningful Gold Analysis;  U.S. 	Geological Survey, Professional Paper, 625-C.Ficklin, W.H. (1970): A Rapid Method for the Determination of 	Fluorine in Rocks and Soils, Using an Ion Selective 	Electrode; U.S. Geological Survey, Paper 700C, pp. C186-188.Harris, J.F. (1982): Sampling and Analytical Requirements for 	Effective use of Geochemistry in Exploration for Gold;   	Precious Metals in the Northern Cordillera; in Symposium 	proceedings, A.A., Levinson, Editor; Association of 	Exploration Geochemists and Geological Association of Canada, 	Cordilleran Section, pp. 53-67.Holland, S.S. (1976): Landforms of British Columbia, A 	Physiographic Outline; B.C. Ministry of Energy, Mines and 	Petroleum Resources, Bulletin 48.Jonasson, I.R., Lynch, J.J. and Trip, L.J. (1973) Field and 	Laboratory Methods used by the Geological Survey of Canada in 	Geochemical Surveys: No. 12, Mercury in Ores, Rocks, Soils, 	Sediments and Water; Geological Survey of Canada, Paper 73-	21.Mihalynuk, M. and Smith, M. (1993): Geology compilation of map 	sheet 104M - Skagway (unpublished).Plant, J. (1971): Orientation Studies on Stream Sediment Sampling 	for a Regional Geochemical Survey in Northern Scotland, 	Institute of Mining and Metallurgy, Transactions, Volume 80, 	pp. B324-345.