Province of British Columbia
Ministry of Energy, Mines and Petroleum Resources

     Mineral Resources Division
     Geological Survey Branch
     Environmental Geology Section


          File:   FORMAT.DOC
          Date:   August 4, 1993


FORMAT SPECIFICATION - REGIONAL GEOCHEMICAL SURVEY (RGS) DATA


BC RGS 37 - NTS 104M  Skagway ...


This document describes the data format for recorded field
observations and analytical data, with an explanation of the
codes for the field observations.


PLEASE NOTE:

1. Data for each sample are listed on single, fixed length
   lines.

2. The data format described in this document represents the
   most recent (August,1993) version.  Missing field data are 
   listed as a blank and missing analytical data are listed as
   -1.  Please note that U, W, Sn and Cr by AAS and Zr by INAA
   were not included as part on the 1993 analytical suite of 
   elements and are listed as -1. 

3. The listed UTM sample site coordinates for map sheet 104M    
   were digitized from the original 1:50 000 scale sample 
   location field maps. 


***** FIELD DATA *****


FIELD DESCRIPTION            COLUMNS  TYPE  LENGTH  EXAMPLE

01  NTS Map-Sheet            001-006   A      6      104M13
02  ID   (Year,Crew,Number)  007-012   N      6      921102
03  UTM Zone                 013-014   N      2      10
04  UTM East      (Metres)   015-020   N      6      296410
05  UTM North     (Metres)   021-027   N      7      5433351
06  Elevation     (Metres)   028-031   N      4      1500
07  Sample Material          032       N      1      6
08  Replicate Status         033-034   N      2      10
09  Formation                035-038   A      4      EKgd
10  Source of Water          039       N      1      2
11  Stream Order             040       N      1      1
12  Stream Type              041       N      1      2
13  Physiography             042       N      1      3
14  Drainage Pattern         043       N      1      2
15  Contamination            044       N      1      3
16  Stream Width (metres)    045-048   N      4 (1)  10.5
17  Stream Depth (cm)        049-051   N      3      220
18  Stream Flow Rate         052       N      1      1
19  Water Colour             053       N      1      3
20  Bank Type                054       N      1      3
21  Bank Precipitate         055       N      1      2
22  Sediment Composition     056-058   N      3      111
23  Sediment Colour          059       N      1      5
24  Sediment Precipitate     060       N      1      2
25  Channel Bed Type         061       N      1      3
26  Channel Pattern          062       N      1      4
27  Date (day/month)         063-066   N      4      2510


***** ANALYTICAL DATA *****


FIELD DESCRIPTION            COLUMNS  TYPE  LENGTH  EXAMPLE

28  pH of stream waters      067-072   N      6 (1)    7.0
29  Uranium in waters (ppb)  073-078   N      6 (2)    0.12
30  Fluoride in waters(ppb)  079-084   N      6       34
31  Sulphate in waters(ppm)  085-090   N      6 (1)   12.4 
32  Zinc              (ppm)  091-096   N      6       47
33  Copper            (ppm)  097-102   N      6       79
34  Lead              (ppm)  103-108   N      6       12
35  Nickel            (ppm)  109-114   N      6       26
36  Cobalt            (ppm)  115-120   N      6       33
37  Silver            (ppm)  121-126   N      6 (1)    1.7
38  Manganese         (ppm)  127-132   N      6      310
39  Iron              (%)    133-138   N      6 (2)    3.80
40  Molybdenum        (ppm)  139-144   N      6       10
41  Uranium           (ppm)  145-150   N      6 (1)    4.5
42  Tungsten          (ppm)  151-156   N      6        6
43  Tin               (ppm)  157-162   N      6        5
44  Mercury           (ppb)  163-168   N      6       30
45  Arsenic           (ppm)  169-174   N      6 (1)   14.5
46  Antimony          (ppm)  175-180   N      6 (1)    0.3
47  Cadmium           (ppm)  181-186   N      6 (1)    0.7
48  Vanadium          (ppm)  187-192   N      6        7
49  Bismuth           (ppm)  193-198   N      6 (1)    0.6
50  Chromium          (ppm)  199-204   N      6       88
51  LOI               (%)    205-210   N      6 (1)    8.3
52  Fluorine          (ppm)  211-216   N      6      400 


**** INAA DATA ****


53  Gold(1st analysis)(ppb)  217-222   N      6       78
54  Gold (Repeat)     (ppb)  223-228   N      6      200
55  Antimony          (ppm)  229-234   N      6 (1)    1.7
56  Arsenic           (ppm)  235-240   N      6 (1)    8.9
57  Barium            (ppm)  241-246   N      6      850
58  Bromine           (ppm)  247-252   N      6 (1)   29.5
59  Cerium            (ppm)  253-258   N      6       18
60  Cesium            (ppm)  259-264   N      6        6
61  Chromium          (ppm)  265-270   N      6       36
62  Cobalt            (ppm)  271-276   N      6       14
63  Hafnium           (ppm)  277-282   N      6       12
64  Iron              (%)    283-288   N      6 (2)    7.57
65  Lanthanum         (ppm)  289-294   N      6       11
66  Lutetium          (ppm)  295-300   N      6 (2)    0.65
67  Molybdenum        (ppm)  301-306   N      6       10
68  Nickel            (ppm)  307-312   N      6       39
69  Rubidium          (ppm)  313-318   N      6      110
70  Samarium          (ppm)  319-324   N      6 (1)    8.2
71  Scandium          (ppm)  325-330   N      6 (1)   20.5
72  Sodium            (%)    331-336   N      6 (2)    3.24
73  Tantalum          (ppm)  337-342   N      6 (1)    1.9
74  Terbium           (ppm)  343-348   N      6 (1)    0.8
75  Thorium           (ppm)  349-354   N      6 (1)    7.6
76  Tungsten          (ppm)  355-360   N      6       12
77  Uranium           (ppm)  361-366   N      6 (1)   28.5
78  Ytterbium         (ppm)  367-372   N      6 (1)   21.3
79  Zirconium         (ppm)  373-378   N      6      560
80  Sample Weight     (g)    379-384   N      6 (2)   19.35

Significant digit/s for data variables listed in brackets.

EXPLANATION OF CODES FOR FIELD OBSERVATIONS

FIELD  COLUMNS  DESCRIPTION

01     001-006  NTS MAP-SHEET:
                National Topographic System (NTS)
              
02     007-012  ID / SAMPLE NUMBER:
                Consists of three parts, 
                Collection Year,               (COL 07-08)
                then Field Party Number,       (COL 09   )
                then a Sequential Number       (COL 10-12)

       013-027  SAMPLE SITE LOCATION:
                Utilizes the Universal Transverse Mercator 
                (UTM) System and consists of three parts,
03              UTM Zone,                    (COL 13-14)
04              UTM Eastings,                (COL 15-20)
05              UTM Northings                (COL 21-27)

06     028-031  ELEVATION:
                Elevation at the sample site (metres).

07     032      SAMPLE MATERIAL:
                Nature of media sampled.
               1 - Stream Sediment    6 - Water and Sediment

08     033-034  REPLICATE STATUS:
                Relationship of current sample to others.
                 0 - Routine sample site
                10 - First of a field duplicate pair
                20 - Second of a field duplicate pair

09     035-038  GEOLOGICAL FORMATION: 
                Formation underlying sample site.
                Refer to 104M.DOC for coded geological
                formations.

10     039      STREAM SOURCE:
                0 - Unknown          2 - Spring run-off
                1 - Groundwater      3 - Glacier melt water

11     040      STREAM ORDER:
                1 - Primary          3 - Tertiary
                2 - Secondary        4 - Quaternary

12     041      STREAM TYPE:
                1 - Permanent        3 - Re-emergent
                2 - Seasonal

13     042      PHYSIOGRAPHY:
                General topography of sampled catchment area
                0 - Lowland Plain    3 - Hilly, Undulating
                1 - Muskeg, Swamp    4 - Mountains, Mature
                2 - Peneplain,       5 - Mountains, Youthful
                    Plateau

14     043      DRAINAGE PATTERN:
                1 - Dendritic        4 - Interrupted
                2 - Herringbone      5 - Glacially Deranged
                3 - Rectangular

15     044      CONTAMINATION:
                Degree or type of Human Contamination
                0 - None               3 - Agriculture
                1 - Possible/Probable  4 - Domestic
                2 - Mining             5 - Forestry

16     045-048  STREAM WIDTH:
                Width of the stream (bank full) at the 
                sample site in metres

17     049-051  STREAM DEPTH:
                Depth of the stream (bank full) at the 
                sample site in centimetres.

18     052      STREAM FLOW RATE:
                Visual estimate of stream flow velocity.
                0 - Stagnant           3 - Fast
                1 - Slow               4 - Torrent
                2 - Moderate

19     053      STREAM WATER COLOUR:
                0 - Colourless         2 - White cloudy
                1 - Brown, clear       3 - Brown cloudy

20     054      BANK TYPE:
                General Nature of the bank material.
                0 - Unknown            4 - Glacial outwash
                1 - Alluvial           5 - Bare rock
                2 - Colluvial          6 - Talus, Scree
                3 - Till               7 - Organic

21     055      BANK PRECIPITATE:
                Presence of stain, weathering; bloom on 
                rocks in the area surrounding the sample 
                site.
                0 - None, otherwise same codes as sediment 
                          colour.

22     056-058  SEDIMENT COMPOSITION:
                Bulk composition of the collected sample as 
                a function of abundance of sand, fines and 
                organics.
                0 - Absent             2 - Medium 33-67%
                1 - Minor < 33%        3 - Major  >67%

                % Sand                   (COL 56)
                % Fines, Silt and Clay   (COL 57)
                % Organics               (COL 58)

23     059      SEDIMENT COLOUR:
                General colour of collected sediment.
                1 - Red                5 - Green
                2 - White, Buff        6 - Gray, Blue
                3 - Black              7 - Pink
                4 - Yellow             8 - Tan, Brown

24     060      SEDIMENT PRECIPITATE OR STAIN:
                Presence of any coatings on gravels,
                pebbles,boulders within the sample,
                or on stream bottoms at the sample site.
                0 - None, otherwise same codes as 
                    sediment colour.

25     061      CHANNEL BED:
                Texture of channel bed.
                1 - Boulders           3 - Sand and Gravels
                2 - Fine Sand to Clay  4 - Organics

26     062      CHANNEL PATTERN:
                1 - Shoots and Pools   3 - Meandering
                2 - Braided            4 - Disturbed

27     063-066  DATE
                Date sample collected, day/month.

28-79  067-384  ANALYTICAL DATA