GSC OPEN FILE D3685

REGIONAL STREAM SEDIMENT AND WATER DATA, CENTRAL YUKON

NTS 105M and 105N

INTRODUCTION

This open file presents data from 1 742 stream sediment samples collected in 1987, 1988 and 1990 from central Yukon.  These samples were reanalysed for bismuth and selenium.  The analytical costs were funded by the Yukon Geology Program, a cost-shared agreement between the Department of Indian Affairs and Northern Development and the Government of Yukon.

Analytical results and field observations are used to build a national geochemical database for resource assessment, mineral exploration, geological mapping, and environmental studies.  Sample collection, preparation procedures and analytical methods are strictly specified and carefully monitored to ensure consistent and reliable results regardless of the area, the year or the analytical laboratory.

CREDITS

P.W. Friske directed the reanalysis program.

Contracts were let to the following companies for sample collection, preparation and analysis:

Analysis:	CanTech Laboratories Inc.

Calgary, Alberta

DESCRIPTION OF SURVEY AND SAMPLE

MANAGEMENT

Sample site duplicate samples were routinely collected in each analytical block of twenty samples.  Field observations were recorded on standard forms used by the Geological Survey of Canada (Garrett, 1974).

Site positions were marked on 1:50 000 scale NTS maps in the field and later digitized at the Geological Survey in Ottawa to obtain Universal Transverse Mercator (UTM) coordinates.

Field-dried samples were air-dried and sieved through a minus 80 mesh (177 micron) screen before milling in ceramic-lined puck mills.  At this time, control reference and blind duplicate samples were inserted into each block of twenty sediment samples.  Analytical data from labs were monitored for reliability with standard methods used by the Applied Geochemistry Subdivision at the Geological Survey of Canada.

ANALYTICAL PROCEDURES

A 1000 mg portion of prepared sample was digested in an acid mixture (3:1 nitric :  hydrochloric acids) in a water bath at 90( C for 2 hours.   After cooling, adjusting the final volume and allowing the solids to settle, an aliquot of solution was removed and analysed for bismuth and selenium by flameless atomic absorption spectrometry using sodium hydride as reductant.   The hydrides were passed through a heated quartz cell where the absorption was measured.

Table 1.  Summary of Analytical Data and Methods

| ELEMENT | DETECTION LEVEL | METHOD |
| --- | --- | --- |
| SEDIMENTS: Bi Bismuth Se Selenium | 0.1 ppm 0.1 ppm | AAS AAS |

FIELD DATA LEGEND

Table 2 describes the field and map information appearing on the following pages preceding the analytical data for each sample site.

REFERENCES

Garrett, R.G.

1974:	Field data acquisition methods for applied geochemical surveys at the Geological Survey of Canada; Geol. Surv. Can. Paper 74-52.

Table 2.  Field Observations Legend

| FIELD RECORD | DEFINITION | TEXT CODE |
| --- | --- | --- |
| Uniq_ID | Unique sample identifier | 105M871002 |
| GSC_OF | Geological Survey of Canada Open File Number | 1962, 2363 |
| NTS_Sht | National Topographic System (NTS); lettered quadrangle (1:250 000 or 1:50 000 scale) | 105M, 105N |
| Sample | Remainder of sample number: Year of collection Field crew Sample sequence number | 89 1,3 001-999 |
| Rep_Stat | Replicate status; relationship of the sample to others within the survey: Routine sample site First of a site duplicate pair Second of a site duplicate pair | 0 1 2 |
| Latitud27 | Latitude (NAD 27) |  |
| Longitud27 | Longitude (NAD 27) |  |
| Sam_Type | Sample material collected: Stream bed sediment only Spring or sediment seep Heavy mineral concentrate Stream water only Natural groundwater, spring seep Simultaneous stream sediment and water Simultaneous spring or seep water and sediment | SedOnly SpgSedOnly HvMnCn Strm GrWat Sed/Water SpgSep/Sed |
| Stm_wdth | Stream width in metres |  |
| Stm_dpth | Stream depth in decimetres |  |
| Contam | Contamination, human or natural: None Possible Probable Definite Mining activity Industrial sources Agricultural Domestic or household Forestry activities Burned areas | - Possible Probable Definite Mining Industry Agricult Domestic Forestry Burn |
| Bnk_type | Bank type; the general nature of the bank material adjacent to the sample site: Alluvial Colluvial (bare rock, residual or mountain soils) Glacial till Glacial outwash sediments Bare rock Talus scree Organic predominant (debris, peat, muskeg, swamp) | Alluv Colluv Till Outwash BareRock TalScr Organic |
| Wat_colo | Water colour; the general colour and suspended load of the sampled water: Clear Brown transparent White cloudy Brown cloudy | Clear BnTrans WhCldy BnCldy |
| Stm_flow | Water flow rate: Stagnant Slow Moderate Fast Torrential | Stagnt Slow Modert Fast Torrnt |
| Sed_colo | Predominant sediment colour: Red-brown White-buff Black Yellow Green Grey, blue grey Pink Buff to brown Brown | Rd-Bn Wh-Bf Black Yellow Green Gy-Blu Pink Bf-Bn Brown |
| Sed_Cmp | Sediment composition; description of the bulk mechanical composition of the collected sample on a scale of 1 to 3, the total of the column must add up to 3 or 4 or 5: Size fractions are divided as follows: Column 1 >0.125 mm (sand) Column 2 <0.125 mm (fines - organic silt, clay) Column 3 organic material Amount of size fraction: sum of amounts = 3 4 5 Absent 0 0 0 Minor <33% 25% 20% Medium 33-67% 50% 40% Major >67% 75% 60% | 0 1 2 3 |
| Bot_Pcpt | Precipitate or stain; the presence of any coatings on pebbles, boulders or stream bottoms: None Red-brown White or buff Black Yellow Green Grey Pink Buff to brown | - Rd-Bn Wh-Bf Black Yellow Green Grey Pink Bf-Bn |
| Bnk_Pcpt | Distinctive precipitate, stains or weathering on rocks in immediate area of catchment basin or stream bank: None Red, brown (eg. Fe) White, buff (eg. CO3, Zn) Black (e.g. Fe, Mn, sulphides) Yellow (e.g. Pb, U, Fe, Mo, REE) Green (Cu, Ni, U, Mo, As, Fe) Bluish (Zn, P) Pink (Co, As) | - Rd-Bn Wh-Bf Black Yellow Green Blue Pink |
| Stm_Phys | General physiography of the drainage basin: Plain Muskeg, swampland Peneplain, plateau Hilly, undulating Mountainous, mature Mountainous, youthful (precipitous) | Plain Swamp Penpln Hill Moun/M Moun/Y |
| Stm_Dran | Drainage pattern: Poorly defined, haphazard Dendritic Herringbone Rectangular Trellis Discontinuous shield type (chains of lakes) Basinal Others | Poor Dendrc Herrbn Rectln Trellis Discnt Closed Other |
| Stm_Type | Stream type: Undefined Permanent, continuous Intermittent, seasonal Re-emergent, discontinuous | Undfnd Permnt Intermit Re-emerg |
| Stm_Class | Classification based on proximity to source: Undefined Primary Secondary Tertiary Quaternary | Undfnd Pri'ary Sec'ary Ter'ary Qua'ary |

| Wat_Sorc | Source of water: Unknown Groundwater Snow melt or spring run-off Recent precipitation Ice-cap or glacier meltwater | Unknown Ground Sp'gMelt RecRain Glacier |
| --- | --- | --- |