Ted Tullis Placer Evaluation

Daily Log

Crew:	Scott Casselman – Crew Chief

Peter Malacarne – Assistant

Friday, Sept 21	SC and PM finish loading gear and drive to Carmacks. Meet with Brian Parsons and continue to Minto Landing to unload truck at staging area.  SC drives truck back to Carmacks and heli to staging area.  Brian slings gear to Sunshine Ck then PM and SC with internal load.  Set-up camp until bed time.

Sat, Sept 22	Cold in morning, minor hail on ground, clear and sunny.  Finish setting up camp unitl noon, then scout out area looking for lease lines or posts.  Locate 2 4x4 posts lying on ground at base of tree approx 65 m from Junction  of Isaac and Sunshine creeks – no marking on them, no flagging, no marked lines found.

Sun, Sept 23	Cold in morning, minor hail on ground, clear and sunny.  Begin cutting baseline for Grid 1 120 m south of camp (Lower Isaac Creek).  Run baseline at 250 degrees and cut it to near jct of Sunshine and Isaac creeks.  Origin of grid (0 N, 0 E) located 30 m south of two posts found lying on ground.

Production: 750 m of cutting

Mon., Sept 24	Cold in morning, ice on still water, clear and sunny.  Continue cutting baseline for Grid 3, up Sunshine Creek.  Start at same origin as for Grid 1 and run baseline at bearing of 280 degrees.

Production: 500 m of cutting

Tues, Sept 25	Cold in morning, ice on still water, clear and sunny warm in afternoon.  Finish cutting Grid 3 Baseline to 1200 W.

Production: 700 m of cutting

Wed, Sept 26	Cold in morning, ice on still water, clear and sunny warm in afternoon.  Start on baseline for Grid 2 (Upper Isaac Creek) from origin of Grid 1 and 3.  Baseline at orientation of 205 degrees, cut from 0 W to 800 W.

Production: 800 m of cutting

Thur, Sept 27	Cold in morning, ice on still water, clear and sunny warm in afternoon.  Finish baseline for Grid 2 at 1100 W.  Locate some old axe cut trees at creek and one piece of relatively new (1 to 2 years old) pink flagging on ground.  Run lines 1000 W and 900 W to creek and drop trees for bridges.  Continue down Isaac Ck and drop trees  at approximate 100 m intervals  for crossings.

Production: 300 m of cutting, 200 m of line

Fri, Sept 28	Cold in morning, ice on still water, clear and sunny warm in afternoon.  Finish baseline for Grid 1 from 750E to 1000 E. Cut trees  for bridge crossings.

Production: 250 m of cutting

Sat, Sept 29	Cold in morning, ice on still water, clear and sunny warm in afternoon.  Run lines on east side of grid 1. From 1000 E to 250 E.

Production: 4260 m of line

Sun, Sept 30	Cold in morning, ice on still water, clear and sunny warm in afternoon,cloding over late in day.  Run lines on west side of Grid 1 and east side of Grid 3. From 250 E to 300W.

Production: 5720 m of line

Mon, Oct 1	Overcast  all day, warmer in am, but did not warm-up at all through day.  Run lines on west side of Grid 3 and east side of Grid 2.

Production: 4800 m of line

Tue, Oct 2	Snow and freezing rain in early am, sun came out around 1:00 clear in afternoon and warmer.  Run lines on west side of Grid 2  - slow going in wet bush.

Production: 4200 m of line

Wed, Oct 3	Overcast most of day and cool.  SC runs mag on grid 3 and 2 lines on Grid 2.  PM finishes running lines on Grid 2.

Production: 1960 m of line

7000 m of mag

Thur, Oct 4	Overcast in AM clear and cool in afternoon.  PM runs mag on grid 2.  SC starts pitting anomaly on grid 3 at 450W/100S.  Digs to 1.7 m – hits water table.  Collects 1 sample.

Production: 4120 m of mag, 1 pit

Fri, Oct 5	Clear and mild in AM, warm in afternoon.  PM finishes mag on grid 2 and moves to Grid 1.  SC completes pit on grid 3 at 450W/100S and starts pit on Grid 2 at L100W/80N.

Production: 3420 m of mag, 1 pit

Sat, Oct 6	Rain in night, clearing and mild in AM, warm in afternoon scattered shower.  PM does mag on grid 1.  SC works on pit 2 on grid 2 at L100W/80N.  Pit to 2.15 m – need to crib.

Production: 5120 m of mag

Sun, Oct 7	Overcast all day and cold.  PM finishes mag on grid 1 then goes to help on Pit 2.  SC works on pit 2.

Production: 1580 m of mag

Mon, Oct 8	Light snow in night and through morning and early afternoon, clearing later in day.  SC and PM crib Pit 2 and deepen to 2.5 m.

Production: 0.5 m of pitting

Tue, Oct 9	Overcast and cool in morning.  SC and PM pitting at Pit 2 and deepen to 3.0  m.  Run into to water – unable to bail fast enough.

Production:  0.5 m of pitting

Wed, Oct 10	Overcast and cool, clear in afternoon.  Collect sample from bottom of pit and pan for concentrate.  Tear down kitchen tarp and pack-up gear for de-mob I late afternoon.

Thur, Oct 11	Clear and cold.  Pack-up tent and gear in morning.  Helicopter arrives at 11:00 for demob.  Drive from Carmacks to Whitehorse at 4:00 in afternoon.